## Slide 1
國立臺灣大學 奈米機電系統研究中心 National Taiwan University Nano-Electro-Mechanical-Systems (NEMS) Research Center

## Slide 2: 臺灣大學卓越研究大樓

## Slide 3: 卓越研究大樓簡介 Complex for Research Excellence
目標：「提供完善的研究空間以培育跨領域性研究人才與 基本技術以促進本校之學術研究發展」
  研究主軸：理工科技及生農科學
    半導體實驗室（2樓無塵室）
    材料分析實驗室（虛擬實驗室）
    生物基因實驗室（虛擬實驗室）
任務
  落實共通性實驗室制度
  鼓勵跨院系整合性研究發展
  爭取產業合作以利永續經營

## Slide 4: 卓越研究大樓位置
NTU main Campus
台大水源校區

## Slide 5: 卓越研究大樓樓層規劃
樓層 | 空 間 別 | 坪 | 樓板面積(m2) | 樓高(m)
B2 | 機電設備/地下停車場 | 792 | 2,618 | 4
B1 | 機電設備/地下停車場 | 792 | 2,618 | 4
1F | 行政辦公室、精密實驗室、會議室、討論室、名人堂 | 479 | 1,583 | 6
2F | 無塵室、機電設備 | 405 | 1,338 | 6.5
3F | 實驗研究室(未來可改建為無塵室) | 464 | 1,533 | 6.5
4F | 會議室/實驗研究室 | 343 | 1,090 | 5.5
5-10F | 實驗研究室/討論室 | 約380/層 | 約1,200/層 | 4
總計 |  | 5,543 | 18,324 | 56.5

## Slide 6: 卓越研究大樓1F平面圖
精密儀器實驗室
精密儀器實驗室
精密儀器實驗室
教學教室
會議室
討論室
辦公室
名人堂
休息區
大聽入口
樓梯2
樓梯1
電梯

## Slide 7: 卓越研究大樓2F平面圖
爐管區CVD
薄膜區PVD
乾蝕刻區
分析區
蝕刻區
Class 100
黃光區
更衣區
212辦公室
廁所

## Slide 8: 卓越研究大樓2F平面圖
休息區實驗室
爐管區
薄膜區
乾蝕刻區
分析區
濕蝕刻區
Class 100
黃光區
更衣區
滅火器
逃生門

## Slide 9: 卓越研究大樓2F平面圖
休息區實驗室
爐管區
薄膜區
乾蝕刻區
分析區
濕蝕刻區
Class 100
黃光區
更衣區
緊急沖洗區
敵腐靈&六腐靈

## Slide 10
無塵室開放時間
每日凌晨六時至晚上十二點整。
無塵室關廠時間
農曆過年期間。
台北市政府公告颱風停止上班上課期間。
停電期間或台大無預警跳電。
自來水公司停水期間或地震後。
其他（儀器或廠務設備保養期間，將於本中心公告關廠時間）。
無塵室運作時間
(如需要在非開放時間使用，請聯絡本中心進行申請)
(關廠後，本中心會公告復廠時間，始得進入使用無塵室)

## Slide 11
服裝安全規定
無塵衣穿著法

## Slide 12: 現場設備照片

## Slide 13: 現場廠務照片

## Slide 14
Process | Equipment | Company | Type | Size | 目前位置
Photolithography | Manual Mask Aligner | SUSS | MABA6 | 6 | 卓越
 | Manual Mask Aligner | SUSS | MABA8 Gen3 | 4(8) | 卓越
 | Maskless laser lithography | Heidelberg | DWL 2000 | 9 | 卓越
 | Spin Coater x 2 | Laurell and科毅 |  | 4-6 | 卓越
 | Hot plate | 科毅 |  | 8 | 卓越
Dry Etching | ICP-RIE | Samco | RIE 800 iPB | 8 | 卓越
 | ICP-RIE | Oxford | PlasmaPro system100 ICP-180 | 8 | 卓越
 | RIE | Oxford | PlasmaPro system100 | 8 | 卓越
 | RIE | Samco | RIE-10N | 4 | 應力
Equipment Table (1)

## Slide 15
Equipment Table (2)
Process | Equipment | Company | Type | size | 目前位置
Thin Film | RTA | Premtek |  | 6 | 卓越
 | PECVD | Oxford | PlasmaPro system100 | 8 | 卓越
 | LPCVD and APCVD | Tempress | TS6603BM | 4(6) | 卓越
 | E-Gun (Meta) | 高敦 |  | 4 | 卓越
 | E-Gun (Oxide) | 高敦 |  | 4 | 卓越
 | Sputter | 高敦 |  | 4 | 卓越
Package | Substrate Bonder | SUSS | SB-6e | 6 | 卓越
Measurement Systems | Surface profiler | 原力 | STEP-4s | 4 | 卓越
 | Semiconductor Device Analyzer | Keysight | B1500A | 4 | 卓越
 | 3D Laser Scanning Microscope | Keyence | VK-X210 | 4 | 卓越
 | Ellipseometer | Horiba | AutoSE | 4 | 卓越
 | SEM、EDS | Hitachi | S4800 | 4 | 卓越

## Slide 16
Maskless laser lithography system
HEIDELBERG DWL 2000
Max. substrate: 9” × 9”
writing area: 20 × 20 cm2
Substrate thickness: 0-7 m
Min. structure size: 0.8 μm
Max. writing speed: 1.1 cm2/min
Position resolution: 10nm
Gray scale exposure mode
已知使用單位:奇景光電

## Slide 17
Manual Mask Aligner
SUSS MABA6
SUSS MABA8 Gen3
SUSS MABA8 Gen3
Mask dimension: 3”~6”
Wafer size: ~4“
Exposure size: 8"
Lamp: 1000 W
Exposure intensity:
>50 mW/cm2 (G), >30 mW/cm2
Alignment system: Double side
Resolution: 1.5~3.5 m
SUSS MABA6
Mask dimension: 3”~7”
Wafer size: ~6“
Exposure size: 6"
Lamp: 350 W
Exposure intensity:
>32 mW/cm2 (G), >12 mW/cm2
Alignment system: Double side
Resolution: 0.8~2.5 m

## Slide 18
OXFORD PlasmaPro system100 ICP 180
OXFORD PlasmaPro system100
  Oxford ICP-RIE system
  ICP RF: 13.56 MHz 3000 W
  Substrate RF: 13.56 MHz 300 W
  Processing gas: He、O2、Ar、SF6、CH4、H2
  Material: Si, GaAs, InP, III-V materials
  Wafer size: ~8”
  Oxford RIE system
  Substrate RF: 13.56 MHz 300 W
  Processing gas: He、O2、Ar、CF4、CHF3
  Material: SiO, SiN
  Wafer size: ~8”
  3-S plasma descum system
  Substrate RF: 13.56 MHz 600 W
  Processing gas: O2、Ar、CF4、CHF3
  Material: Si
  Wafer size: ~4”
  3-S plasma descum system
  Substrate RF: 13.56 MHz 300 W
  Processing gas: O2、Ar
  Material: Photoresist
  Wafer size: ~4”
  Samco ICP-RIE system
  ICP RF:
  13.56 MHz 3000 W
  Substrate RF:
  13.56 MHz 500 W
  Processing gas:
  He、O2、Ar、SF6
  、CF4、C4F8
  Material: Si materials
  Wafer size: ~8”
Samco RIE 800 iPB
Plasma etching system (Dry Etching)

## Slide 19
Horizontal furnace (APCVD & LPCVD)
TEMPRESS TS6603BM
Diffusion process:
(APCVD)
• Dry/ wet oxide
• Anneal
Deposition process:
(LPCVD)
• Poly silicon
• Silicon nitride
• LTO
Wafer size: 4”
(possible upgrade to 6”)
Process wafer load: 25
(possible upgrade to 100 wafers)

## Slide 20
Plasma Enhanced Chemical Vapor Deposition
(PECVD)
OXFORD PlasmaPro system100 PECVD
Substrate RF：
13.56 MHz 600 W
Processing gas：
CF4, NH3, SiH4
Deposition process：
• SiO2
• SiNx
• Amorphous silicon
Thickness：
30~1000nm
Max. wafer size:
8" (uniformity <5%)

## Slide 21
Physical Vapor Deposition systems
(PVD)
E-gun evaporator for metal material
E-gun: 6kW
Crucible Liners: 15 cc for 6 pieces
Vacuum: 510-7 Torr
Sample size: 3”6, 4”5, 2”~3”8
E-gun evaporator for oxide
E-gun: 6kW
Crucible Liners: 15 cc for 6 pieces
Vacuum: 510-7 Torr
Sample size: 3”6, 4”5, 2”~3”8
Sputter system:
RF target: 600 w for 2 unit
DC target: 1000 w for 2 unit
Vacuum: 510-7 Torr
Sample size: 4”

## Slide 22
Wafer size: ~ 6”
Temperature range: RT ~ 1250℃
Temperature ramp up rate:
>150℃/sec (Bare Wafer)
>50 ℃/sec (with graphite tray)
Temperature uniformity: ±1%
Process pressure：10m Torr ~ 1 atm
Process gas: Ar, N2, O2
Rapid thermal process
(RTP)
Premtek RTP

## Slide 23
Substrate Bonder
Wafer size: ~6”
Bond Processes
• Anodic Bonding
• Eutectic Bonding
• Glass Frit Bonding
• Fusion Bonding(post bond annealing required)
• Thermo-compression
• SOI Bonding
• Adhesive Bonding(various adhesives)
• Temporary Bonding Applications
Low Temperature Methodologies
• Eutectic Bonding
• Fusion Bonding(post bond annealing required)
• Thermo-compression
• Adhesive Bonding (photo definable),
• Benzocyclobutene (BCB), SU8 resist
SUSS SB6e

## Slide 24
Surface profiler
Force STEP-4s
Scan length range: 9 mm
Vertical scan range: 180 μm
Max. scan speed: 500 μm/s
Vertical resolution: 0.2 nm
Repeatability: <2 nm+ 0.1% step height
Probe tip radius: 2μm
Min. contact force: 0.1 mg
Stage size: ~4” auto X-Y stage
Keyence VK-X210
3D Laser Scanning Microscope
Optical zoom: 1x to 8x
Objective lens magnification:
10x, 20x. 50x, 150x
Magnification on a 15” monitor:
200x, 400x, 1000x, 3000x
Vertical range: 7 mm
Vertical resolution: 0.5 nm
Width resolution: 1 nm
Stage size: ~6” auto X-Y stage
Morphology Measurement Systems

## Slide 25
Keysight B1500A
Semiconductor
Device Analyzer
Current versus voltage (IV) measurement
• High resolution source monitor unit (HRSMU)
Range :100 V/0.1 A, Resolution: 0.5 µV/ 1 fA
• High power source monitor unit (HPSMU)
Range :200 V/1 A, Resolution: 2 µV/ 10 fA
• Mid power source monitor unit (MPSMU)
Range :100 V/0.1 A, Resolution: 0.5 µV/ 10 fA
Capacitance measurement:
• Multi power capacitance measurement unit (MPCMU)
AC impedance measurement (C-V, C-f, C-t)
1 kHz to 5 MHz with 1 mHz resolution
Pulsed IV measurement:
• HRSNU, HPSMU, MPSMU
Pulse measurement from 500 μs pulse width
Spectral range: 440-1000 nm
Spot sizes: < 50x60 µm
Sample stage: 200x200 mm
Field of view: 1.33x1 mm
Goniometer: 70° ,possible at 66° & 61.5°
Measurement time: <5s
Accuracy: NIST 100nm d ± 4Å
Repeatability: NIST 15nm ± 0.2 Å
Horiba AutoSE
Ellipseometer
Measurement Systems

## Slide 26: 卓越研究大樓2F平面圖
休息區實驗室
爐管區
薄膜區
乾蝕刻區
分析區
濕蝕刻區
Class 100
黃光區
更衣區
滅火器
逃生門
廁所
有機、鹼槽
Sping coater
AM6、MA8
DWL2000
化學儲放櫃
LPCVD
APCVD
PECVD
O2 plasma
RIE
Oxford ICP-RIE
Samco ICP-RIE
RTA
sputter
E-gun
橢偏儀
confocal
SEM&EDS

## Slide 27: 卓越研究大樓2F平面圖
爐管區CVD
薄膜區PVD
乾蝕刻區
分析區
蝕刻區
Class 100
黃光區
更衣區
實驗室

## Slide 28
上課前三日完成報名並確認有開課後請至應力所200繳費

## Slide 29: 火災緊急防護措施
不要嚐試去撲滅比垃圾桶大小還大的火災
或是已經明顯失去控制的火災
通知救護車
33669595
通知中心人員
33665063
ext. 21~28
通知校警隊
33669110
confocal

## Slide 30: 特殊氣體防護措施
由本中心人員宣佈
實驗室重新開放後
始可進入實驗室。
28
33669110
氣體外洩
現場